## Slide 1: Advanced Digital Signal Processing 高等數位訊號處理
授課者： 丁 建 均
Office：明達館723室, TEL： 33669652
E-mail: jjding@ntu.edu.tw
課程網頁：http://djj.ee.ntu.edu.tw/ADSP.htm
歡迎大家來修課，也歡迎有問題時隨時聯絡！

## Slide 2
 評分方式：
Basic: 15 scores
原則上每位同學都可以拿到 12 分以上，
另外，上課回答問題，每回答一次加1分
Homework: 60 scores (5 times, 每 3 週一次)
請自己寫，和同學內容極高度相同 ，將扣 70% 的分數
就算寫錯但好好寫也會給 40~95% 的分數，
遲交分數打 8 折，不交不給分。 不知道如何寫，可用 E-mail 和我聯絡，或於上課時發問
禁止 Ctrl-C Ctrl-V 的情形。
Term paper 25 scores

## Slide 3
Term paper 25 scores
方式有四種
(1) 書面報告
10頁以上(不含封面)，中英文皆可，11或12的字體，題目可選擇和課程有關的任何一個主題。 格式和一般寫期刊論文或碩博士論文相同，包括 abstract, conclusion, 及 references，並且要分 sections，必要時有subsections。 References 的寫法, 可參照一般 IEEE 的論文的寫法
鼓勵多做實驗及模擬，有創新更好。
嚴禁 Ctrl-C Ctrl-V 的情形，否則扣 70% 的分數
(2) Tutorial (對既有領域做潛顯易懂的整理)
限十八個名額，和書面報告格式相同，但 頁數限制為18頁以上(若為加強前人的 tutorial，則頁數為 (2/3)N + 13 以上，N 為前人 tutorial 之頁數)，題目由老師指定，以清楚且有系統的介紹一個主題的基本概念和應用為要求，為上課內容的進一步探討和補充，交 Word 檔。
選擇這個項目的同學，學期成績加 3分

## Slide 4
(3) 口頭報告
限四個人，每個人 30~45分鐘，題目可選擇和課程有關的任何一個主題。
口頭報告將於 5月27日(第 13 週)進行。有意願的同學，請及早告知，並且在口頭報告之前提供 PowerPoint 檔。
口頭報告時，鼓勵大家提問（包括口頭報告的同學，也可針對其他同學的報告內容提問）。曾經提問的同學，學期成績皆加 0.5 分。
選擇這個項目的同學，學期成績加 2分
(4) 編輯 Wikipedia
中文或英文網頁皆可，至少 2 個條目，但不可同一個條目翻成中文和英文。總計 80行以上。限和課程相關者，自由發揮，越有條理、有系統的越好
選擇編輯 Wikipedia 的同學，請於 6月13日前，向我登記並告知我要編緝的條目(2 個以上)，若有和其他同學選擇相同條目的情形，則較晚向我登記的同學將更換要編緝的條目
書面報告和編輯 Wikipedia，期限是 7月1日

## Slide 5
Tutorial 可供選擇的題目(共 17 個，可以略做修改)
(1) Nonlinear Filter
(2) Mellin Transform
(3) Financial Signal Processing
(4) Synthetic Aperture Radar (SAR) Image Processing
(5) Echo Cancellation Techniques
(6) Speeded-up Robust Feature (SURF) Points for Template Matching
(7) Supervoxel and Video Segmentation
(8) Compressive Sensing (* 加強前人的 tutorial)
(9) Compressive Sensing for Pattern Recognition
(10) Lossless Image Compression
(11) Recent Development of Video Compression

## Slide 6
(12) Stereoscopic Image Processing
(13) Recent Development of Face Recognition
(14) Haze Removal for Digital Images
(15) Light Field Camera
(16) Digital Watermarking
(17) Signal Processing for Electroencephalography (腦電圖)
Tutorial 可供選擇的題目(可以略做修改)

## Slide 7
上課時間：15 週
2/26,
3/4,
3/11, 出 HW1
3/18,
3/25, 交 HW1
4/8, 出 HW2
4/15,
4/22, 交 HW2
4/29, 出 HW3
5/6,
5/13, 交 HW3
5/20, 出 HW4
5/27, Oral
6/3, 交 HW4
6/17, 出 HW5
7/1, 交 HW5 及 term paper
原則上: 3n 週出作業, 3n+2 週繳交
4/1, 6/10 放假

## Slide 8
Download: 請洽台大電信所
http://comm.ntu.edu.tw/matlab/request.php
參考書目
洪維恩，Matlab 7 程式設計，旗標，台北市，2010. . (合適的入門書)
張智星，Matlab 程式設計入門篇，第三版，碁峰，2011.
蒙以正，數位信號處理：應用 Matlab，旗標，台北市，2007.
繆紹綱譯，數位影像處理：運用-Matlab，東華，2005.
預計看書學習所花時間： 3~5 天
Matlab

## Slide 9
研究所和大學以前追求知識的方法有什麼不同？
研究所 : 觀念的學習
大學 :

## Slide 10
Question:
Why should we use the Fourier transform?
Is the Fourier transform the best choice in any condition?

## Slide 11
Contents:
(1) Introduction 1 W
(2) Digital Filter Design (A) 2 W
(3) Digital Filter Design (B) 2 W
(4) Homomorphic Signal Processing 1 W
(5) Applications (A): Acoustics 1 W
(6) Applications (B): Data Compression, Others 2 W
(7) Fast Algorithms: Basis, FFT and Convolution 3 W
(8) Orthogonal Transform (A): Walsh Transform 1 W
(9) Orthogonal Transform (B): Number Theoretic Transform, 1 W
OFDM, CDMA , and Others
I. Introduction

## Slide 12
目標：
(1) 對 Digital Signal Processing 作更有系統且深入的了解
(2) 學習 Digital Signal Processing 幾個重要子領域的基礎知識

## Slide 13
 Filter 的分類
filter
analog
digital
IIR
FIR
MSE (mean square error)
minimax
frequency sampling
Part 1: Filter
(考慮aliasing)
(技術較早開發)

## Slide 14
IIR filter 的優點：(1) easy to design
(2) (sometimes) easy to implement
缺點：
FIR filter 的優點：
缺點：
An FIR filter is impossible to have the ideal frequency response of

## Slide 15
15
 概念：把 convolution 變成 addition
Part 3: Applications of DSP
filter design, data compression (image, video, text), acoustics (speech, music), image analysis (structural similarity, sharpness), 3D accelerometer
Part 2: Homomorphic Signal Processing

## Slide 16
16
 Basic Implementation Techniques
Example: one complex number multiplication
= ? Real number multiplication.
 Part 4: Fast Algorithms
Trade-off: “Multiplication” takes longer than “addition”

## Slide 17
17
 FFT and Convolution
Due to the Cooley-Tukey algorithm (butterflies),
the complexity of the FFT is:
The complexity of the convolution is: 3個 DFTs,

## Slide 18
18
 Walsh Transform
(CDMA)
 Number Theoretic Transform
Question: DFT 的缺點是什麼？
 Part 5: Orthogonal Transforms
DFT 的兩個主要用途:
Orthogonal Frequency-Division Multiplexing (OFDM)
Code Division Multiple Access (CDMA)

## Slide 19
19
Review 1: Four Types of the Fourier Transform
(1) Fourier Transform
,
Alternative definitions
,
(2) Fourier series (suitable for period function)
頻率和 m 之間的關係：
T: 週期

## Slide 20
20
(3) Discrete-time Fourier transform (DSP 常用)
,
t : sampling interval
(4) Discrete Fourier transform (DFT) (DSP 常用)
,
頻率和 m 之間的關係：
where fs = 1/t (sampling frequency)

## Slide 21
21
(1) Fourier transform
time domain
frequency domain
continuous, aperiodic
continuous, aperiodic
(2) Fourier series
continuous, periodic
(or continuous, only the value in a finite duration is known)
discrete, aperiodic
(3) discrete-time Fourier transform
discrete , aperiodic
continuous, periodic
(4) discrete Fourier transform
discrete, periodic
(or discrete, only the value in a finite duration is known)
discrete, periodic
 四種 Fourier transforms 的比較

## Slide 22
22
Review 2: Normalized Frequency
(1) Definition of normalized frequency F:
where fs = 1/t (sampling frequency)
(2) folding frequency f0
t : sampling interval
若以 normalized frequency 來表示， folding frequency = 1/2

## Slide 23
23
For the discrete time Fourier transform
(1) G(f) = G(f + fs) i.e., G(F) = G(F + 1).
(2) If g[n] is real G(F) = G*(F) (* means conjugation)
(3) If g[n] = g[n] (even) G(F) = G(F),
g[n] = g[n] (odd) G(F) = G(F)
只需知道 G(F) for 0  F  ½ (即 0 < f < f0)
就可以知道全部的 G(F)
Analog filter: H(f)

## Slide 24
24
 Discrete time Fourier transform of the lowpass, highpass, and band pass filters
high pass filter
fs (F = 1) F = 0.5 0 (F = 0) F = 0.5 fs (F = 1)
low pass filter ( pass band 在 fs 的整數倍附近 )
fs (F = 1) 0 (F = 0) fs (F = 1)
band pass filter
fs (F = 1) F = 0.5 0 (F = 0) F = 0.5 fs (F = 1)
f = fs/2

## Slide 25
25
 Z-Transform
Compared with the discrete time Fourier transform:
Review 3: Z Transform and Laplace Transform
suitable for discrete signals

## Slide 26
26
Compared with the Fourier transform:
 Laplace Transform
One-sided form
Two-sided form
suitable for continuous signals

## Slide 27
27
Review 4: IIR Filter Design
Two types of digital filter:
(1) IIR filter (infinite impulse response filter)
(2) FIR filer (finite impulse response filer)
There are 3 popular methods to design the IIR filter.

## Slide 28
28
Method 1: Impulse Invariance
白話一點，就是直接做 sampling
analog filter ha(t)
digital filter h[n]
Advantage : Simple
Disadvantage : (1) infinite
(2)

## Slide 29
29
Method 2: Step Invariance
對 step function 的 response 作 sampling
analog filter ha(t)
digital filter h[n]
step function (continuous form)
0
1
step function (discrete form)
t = 0
u(t)
u[n]
n=0
1
1
1
1
1
0
0
0
0
Laplace transform of u(t):
Fourier transform of u(t):
Z transform of u[n]:

## Slide 30
30
Step 1 Calculate the convolution of ha(t) and u(t)
(其實就是對 ha(t) 做積分)
Step 2 Perform sampling for ha,u(t)
Step 3 Calculate h[n] from
Note: Since
so

## Slide 31
31
Advantage of the step invariance method:
＊主要 Advantage:
Disadvantage of the step invariance method:
較為間接，設計上稍微複雜

## Slide 32
32
Method 3: Bilinear Transform
Suppose that we have known an analog filter ha(t) whose frequency response is Ha(f).
To design the digital filter h[n] with the frequency response H(f),
fold  (, )
fnew  (fs/2, fs/2)
 The relation between fnew and fold is determined by the mapping function
fs = 1/t (sampling frequency)
s: index of the Laplace transform
z: index of the Z transform
c: some constant

## Slide 33
33
代入
 Suppose that the Laplace transform of the analog filter ha(t) is Ha,L(s)
The Z transform of the digital filter h[n] is Hz(z)
參考page 25、page26
f
f

## Slide 34
34
fold
fnew/fs
c = 2
fold | − | 0 |  | 1
fnew |  |  |  | 

## Slide 35
35
Advantage of the bilinear transform
Disadvantage of the bilinear transform
analog filter
Ha(f)
digital filter
H(f)
−fs/2
fs/2
−

0
0
fc
−fc
fc,1
−fc,1

## Slide 36
36
附錄一： 學習 DSP 知識把握的要點
(1) Concepts: 這個方法的核心概念、基本精神是什麼
(3) Advantages: 這方法的優點是什麼
(4) Disadvantages: 這方法的缺點是什麼
(5) Applications: 這個方法要用來處理什麼問題，有什麼應用
(6) Innovations: 這方法有什麼可以改進的地方
或是可以推廣到什麼地方
(3-1) Why? 造成這些優點的原因是什麼
(4-1) Why? 造成這些缺點的原因是什麼
(2) Comparison: 這方法和其他方法之間，有什麼相同的地方？
有什麼相異的地方